## Slide 1
Quantifying LBB Margins Using Probabilistic Approach
Min Wang and Xinjian Duan
Candu Energy Inc.
2019 October 23
3rd International Seminar on Probabilistic Methodologies for Nuclear Applications,
2019 October 22-24, Rockville, MD

## Slide 2: Outline
Introduction
Deterministic LBB Analysis
Probabilistic LBB Analysis
Parameter Studies
      Conclusions

## Slide 3: Introduction & Objective
For Design
      LBB has been generally used to demonstrate extremely low probability of rupture and hence to optimize protective hardware – such as pipe whip restraints and jet impingement barriers.
      The regulatory requirements and detailed evaluation procedures vary among OECD/NEA countries. An LBB benchmark activity initiated and led by USNRC staff was conducted in 2019.
      For aging evaluation in Canada
      Deterministic LBB (DLBB) is used in assessments for small bore piping, supplemented by PFM assessment
      For large LOCA safety analysis
        LBB to demonstrate pipe resistance to break
        PFM to estimate frequencies of pipe break
      Objective
      To present a non-PFM based probabilistic LBB (PLBB) methodology

## Slide 4: Typical DLBB Requirements
      Factor of 10 on the leak detection capability
      Factor of 2 on crack length (critical crack length divided by leakage crack length)
      Factor of 1.0 on load when using absolute combination method of maximum loads, or
      Factor of 1.4 on load when using algebra combination method of maximum loads
  Any one of three requirements can be used as acceptance criteria once the other two are satisfied.

## Slide 5: Conservatisms in DLBB
The probability of earthquake occurrence is 1.0
Using bounding value
      Lower bound for material properties
      Upper bound for loads
Safety factors
      Factor on loads (1.4 or 1.0)
      Factor on crack (2.0)
      Factor on leak rate (10.0 or smaller)
Limitations are covered by extreme conservatisms
      WRS: affect crack growth, COD and crack shape
      Potential multiple cracks

## Slide 6: Comparison of Analysis Methods
LCL: leakage crack length
CCL: critical crack length
RCL: reference crack length
DLR: detectable leak rate
No
No

## Slide 7: Benchmark Problem - Inputs
Parameters based on OECD/NEA LBB benchmarking
Pipe geometry: OD = 406.4 mm, t = 40.462 mm
Normal operating conditions: T = 340C, P = 15.5 MPa
Loads
Material properties (A82):
      Sy = 316.5 MPa, Su = 542.4 MPa, E = 196.8 GPa
      +0.386
      J = 524.4 + 586.3 (kJ/m2)
Degradation mechanism: corrosion fatigue
Detectable leak rate (DLR): 0.0608 kg/s
 | Dead Weight | Thermal | SSE
Axial Force | 17.34 kN | -4 kN | 34.7 kN
Bending Moment | 21.59 kNm | 68 kNm | 288.41 kNm

## Slide 8: Benchmark Problem - Results
Canadian procedure
Leak rate calculated using LEAPOR
SRP 3.6.3 Procedure
Case | Stability | CCL | RCL | COD | Leak rate | Leak Factor | Note
1 | NSC | 147.4 | 73.7 | 0.2309 mm | 0.2436 kg/s | 4.0 | Sf =
2 | NSC | 163.5 | 81.7 | 0.2809 mm | 0.3733 kg/s | 6.1 | Sf = Su
3 | EPFM | 182.2 | 91.1 | 0.3512 mm | 0.6634 kg/s | 10.9 | 
4 | FAD-NSC | 148.6 |  |  |  |  | ASME FFS-1
Case | Stability | CCL | RCL | COD | Leak rate | Leak Factor | Note
1 | NSC | 147.4 | 73.7 | 0.2309 mm | 0.2436 kg/s | 4.0 | 
2 | NSC | 163.5 | 81.7 | 0.2809 mm | 0.3733 kg/s | 6.1 | Sf = Su
3 | EPFM | 182.2 | 91.1 | 0.3512 mm | 0.6634 kg/s | 10.9 | 
4 | FAD-NSC | 148.6 |  |  |  |  | ASME FFS-1
Case | Stability | LCL | COD | CCL | Size Factor | Note
1 | NSC | 89.7 | 0.3395 mm | 147.4 | 1.6 | Sf = =
2 | NSC | 89.7 | 0.3395 mm | 163.5 | 1.8 | Sf = Su
3 | EPFM | 89.7 | 0.3395 mm | 182.2 | 2.0 | 
Case | Stability | LCL | COD | CCL | Size Factor | Note
1 | NSC | 89.7 | 0.3395 mm | 147.4 | 1.6 | 
2 | NSC | 89.7 | 0.3395 mm | 163.5 | 1.8 | Sf = Su
3 | EPFM | 89.7 | 0.3395 mm | 182.2 | 2.0 | 

## Slide 9: Probabilistic Analysis

## Slide 10: Remove Conservatisms in LBB
Using bounding value
      Lower bound for material properties
      Upper bound for loads
Safety factors
      Factor on loads (1.4)
      Factor on size (crack length, 2.0)
      Factor on leak rate (10.0)
Using best estimate distributions
      Material properties
      Loads
      Leak rate
Remove all safety factors
      All factors set to 1.0
Deterministic Analysis
Probabilistic Analysis

## Slide 11: Probabilistic Distributions of Material Properties
Uncertainty is considered in material properties and loads
      Sy and Su
           : xLPR A182
          Sy > 250 MPa
          Su < 860 MPa
          Sy < 0.75 Su
Parameter | Distribution | X5 | X50 |  | 
Sy | Lognormal | 316.50 | 468.74 | 0.2388 | 0.7
Su | Lognormal | 542.40 | 638.58 | 0.0992 | 
105 realizations

## Slide 12: Probabilistic Distributions of Loads
Deadweight and internal pressure is considered to be deterministic
Thermal expansion and SSE is considered to be distributed
      Thermal Expansion
      SSE
Parameter | Distribution | X95 | COV | 
Thermal - F | Normal | -4 kN | 5% | -4.36 kN
Thermal - M | Normal | 68 kNm | 5% | 63.83 kNm
SSE – F | Normal | 34.7 kN | 15% | 27.83 kN
SSE – M | Normal | 288.41 kNm | 15% | 231.33 kNm

## Slide 13: Probabilistic Distribution of Calculated Leak Rate
Based on the validation exercises
      Compared against measurements
      Ratio of prediction (LEAPOR) to measurement: ±25%
          Model uncertainty
          Morphology parameters uncertainty
          Measurement uncertainty
Parameter | Distribution | X50 | X95 |  | 
Multiplier | Lognormal | 1.00 | 1.25 | 0 | 0.136
Leak Rate | Lognormal | Prediction | 1.25Predition | Log(Prediction) | 0.136

## Slide 14: Case 0: Best Estimate (1)
The leak rate of the critical crack established from NO+SSE loads.
Monte Carlo Simulation: 105 realizations
LBB is demonstrated when the predicted leak rate greater than detectable leak rate for a critical crack.
1.5% CCL is below the CCL obtained from DLBB analysis.
1.5%

## Slide 15: Case 0: Best Estimate (2)
The predicted leak rate is well above the DLR (0.0608 kg/s) and 10DLR (0.608 kg/s).
The probability of the leak rate smaller than 10 times DLR is extremely low.
Implies the crack can be detected by leak detection system.
Without leak rate uncertainty
With leak rate uncertainty
Prob(<DLR) = 210-195
Prob(<10DLR) = 110-40
Average Leak Rate = 4.5 kg/s
Average Leak Rate = 4.5 kg/s

## Slide 16: Case 1: Including Load Factor (1)
Load factor = 1.4/1.0, size factor = 1.0
The critical crack apparently decreased under the maximum loads established from 1.4 times algebra sum.
The critical crack slightly decreased under the maximum loads established from 1.0 time absolute sum.
1.4 times algebra sum
1.0 time absolute sum

## Slide 17: Case 1: Including Load Factor (2)
The leak rate apparently decreased under the maximum loads established from 1.4 times algebra sum
The predicted leak rate is still well above the DLR (0.0608 kg/s) and 10DLR (0.608 kg/s).
The probability of the leak rate smaller than 10 times DLR is extremely low.
Case 0: Prob(<DLR) = 210-195
Case 1: Prob(<DLR) = 810-119
Case 0: Prob(<10DLR) = 110-40
Case 1: Prob(<10DLR) = 810-14
Note: The probability of Case 1 is even lower if the 1.0 time absolute sum is used as the maximum load.
Average Leak Rate = 3.6 kg/s

## Slide 18: Case 2: Including All Safety Factors (1)
Realistic material properties and loads are used.
Absolute sum is used as the maximum load.
Leak rate is well above detectable leak rate, 0.0608 kg/s, but ~98% below 10 times detectable leak rate.
Case 0: Prob(<DLR) = 210-195
Case 3: Prob(<DLR) = 110-16
Case 0: Prob(<10DLR) = 110-40
Case 3: Prob(<10DLR) = 0.978
1.0 time absolute sum
Average Leak Rate = 0.38 kg/s

## Slide 19: Case 2: Including All Safety Factors (2)
Leak rate is well above DLR, 0.0608 kg/s, but majority are below 10DLR.
The probability of leak rate below 4 times DLR is 5%.
Leak Rate Factor | Conditional Probability of Leak Rate <FactorDLR given EQ
1 | 110-16 (110-19)
2 | 310-6 (310-9)
3 | 210-3 (210-6)
4 | 510-2 (510-5)
5 | 210-1 (210-4)
6 | 510-1 (510-4)
Note: values in () is unconditional probability assuming earthquake occurance is 110-3.
1.0 time absolute sum
Average Leak Rate = 0.38 kg/s
(> 6DLR)

## Slide 20: DLBB Factor vs. Probability of Failure (BBL)
Uncertainty of material properties, loads and leak rate prediction are considered.
The combined factors adopted in DLBB are extremely conservative.
Case | Average Leak Rate Factor | Probability( < DLR ¦ EQ) | Probability( < 10DLR ¦ EQ)
Best estimate | 74.2 | 210-195 | 110-40
Load factor 1.0 / 1.4 | 73.9 / 59.5 | 410-195 / 810-119 | 110-40 / 810-14
Size factor | 6.3 | 910-17 | 0.977
Load factor & size factor | 6.3 | 110-16 | 0.978
Note: Leak rate factor calculated from traditional LBB is 4.0.
- Copyright - © 2018 SNC-Lavalin Inc. and its member companies. All rights reserved. Unauthorized use or reproduction is prohibited.

## Slide 21: Probabilistic Leak Rate Factor
Maintain the load factor and size factor.
The leak rate factor (LRF) is determined by the averaging conditional probability of BBL (break-before-leak), e.g. 5% corresponding to a leak rate factor of 4.
- Copyright - © 2018 SNC-Lavalin Inc. and its member companies. All rights reserved. Unauthorized use or reproduction is prohibited.
Leak Rate Factor | Conditional Probability of Leak Rate <FactorDLR given EQ
1 | 110-16 (110-19)
2 | 310-6 (310-9)
3 | 210-3 (210-6)
4 | 510-2 (510-5)
5 | 210-1 (210-4)
6 | 510-1 (510-4)
Note: values in () is unconditional probability assuming earthquake occurrence is 110-3.
Mean LRF = 6.3

## Slide 22: X|Y Probabilistic Leak Rate Factor
Maintain the load factor and size factor.
The leak rate factor is determined by the (1-X%) failure probability at Y% lower confidence limit.
- Copyright - © 2018 SNC-Lavalin Inc. and its member companies. All rights reserved. Unauthorized use or reproduction is prohibited.
95|Mean LRF = 5.0
95|95 LRF = 3.5
5%
X Y | 90 | 95
95 | 3.6 | 3.5
90 | 3.9 | 3.7
50 | 5.1 | 4.9

## Slide 23: Effects of Material Properties
For DLBB cases, the material properties are spread in the right tail.
Mean:
All: 406 MPa
>10: 512 MPa
Mean:
All: 512 MPa
>10: 623 MPa

## Slide 24: Effects of Loads
The effect of normal operating loads on DLBB is small.
The bending moment of the maximum loads is biased to the lower end. This is possibly due to lower SSE.

## Slide 25: Effects of Leak Rate

## Slide 26: Ranking of Parameters
Using the important factor based on Degree of Separation [1], as defined:
100% and
Where:
f,i is the mean of the samples corresponding to the failures
all,i is the mean of the samples
all,i is the standard deviation of the samples
i is the ith parameter of interest
The results are consistent with the previous parameter studies, with top three are material properties and leak rate.
Ref [1]: D. Somasundaram et al., Sensitivity Analysis Methodology fro Probabilistic Fracture Mechanics Output, SMiRT25, Charlotte, NC, USA, 2019 August 4-9.
 | Sy | Sf | FTHM | MTHM | FSSE | MSSE | LRM
vs,i (%) | 29 | 38 | 0 | 0.61 | 0 | 9 | 23
Rank | 2 | 1 | 6 | 5 | 6 | 4 | 3

## Slide 27: Summary
A probabilistic analysis of LBB is demonstrated.
      The uncertainty of material properties, loads and leak rate prediction are quantified.
      The margin factors adopted in DLBB are extremely conservative.
      Material properties and leak rate have significant effects on DLBB.
      Seismic bending moment has more effects on DLBB than other loads
The concept of probabilistic leak rate factor is proposed.

## Slide 28: Acknowledgements
USNRC for providing the LEAPOR code
Robert Tregoning for developing & leading the OECD/NEA LBB Benchmark.
Candu Energy’s Product Develop Program for funding the study