## Slide 1
Mark Kirk
marktkirk119@gmail.com
Mohammad Modarres
DML International
dmlint@gmail.com
A Review of Best Practices for Application of Probabilistic Fracture Mechanics to Passive Pressure-boundary Components
Presentation to
ASME SC-XI
WGOPC & WGFE
ASME Code Week
Minneapolis Minnesota
6th August 2019
Presentation to the 3rd International Seminar on Probabilistic Methods for Nuclear Applications
22-24 October 2019 ∘ Rockville, Maryland, USA

## Slide 2: Presentation Outline
Motivation for PFM. Why PFM? Why now?
Deterministic vs. probabilistic. Different?
Elements of any PFM analysis
On-going literature review. Goals & process.
Summary & next steps

## Slide 3: Motivation for PFM
Circa 1970s
  Classical determinism
  Every discipline gets its own margin
    Loading over-estimated
    Material resistance under-estimated
    Screening criteria conservatively established
  Conservatism does not limit operability
    Plants are new
    No plant near screening criteria
time
damage
Failure
40 years
Conservative trend curve
Limited data
Current time
True trend curve (unknown)
conservative screening criteria
(based on high loads)

## Slide 4
Meanwhile …
1970s
Today
Aging

## Slide 5: Motivation for PFM
Today
  More data & knowledge support improved models
  Extended plant lifetimes sought
  Existing conservative screening criteria challenged
    Significant operability impacts
  Issues
    Every discipline can no longer have its own margin
    Deterministic approaches
      Common / accepted / entrenched
      Not well suited to quantifying actual risk
  Solution: PFM
time
damage
conservative screening criteria
(based on high loads)
Updated trend curve
(still conservative)
Much more data
Current time
60 years
80 years
40 years
margin
True trend curve
(better-known,
but still unknown)
Failure

## Slide 6: Deterministic vs. Probabilistic Different … or not so much??
Similarities
  Both DFM & PFM have the same parts (loads, endurance, acceptance criteria)
  Both treat uncertainty mathematically
    Deterministic: bounds uncertainty
    Probabilistic: quantifies uncertainty
  All PFM models include deterministic aspects
Differences
  Uncertainty treatment
    Deterministic: Often implied
    Probabilistic: Explicit
  Safety margin quantification
    Deterministic: Impossible or difficult
    Probabilistic: Explicit. Inherent to methodology.
  Codification
    Deterministic: Yes. Many times.
    Probabilistic: Infrequently. Still seen as “new”.
deterministic
probabilistic

## Slide 7: Elements of any PFM Analysis The Analysis Itself
Inputs
Models
connectivity
simulation
acceptance criteria
Decision

## Slide 8: Elements of any PFM Analysis The Analysis Itself
Inputs
having sufficient
evidence
build
validate
Models
connectivity
simulation
acceptance criteria
Decision
Challenges

## Slide 9: Elements of any PFM Analysis The Analysis Itself
Inputs
double-counting
uncertainties
Models
connectivity
simulation
acceptance criteria
Decision
Challenges

## Slide 10: Elements of any PFM Analysis The Analysis Itself
Inputs
verification and
validation
Models
connectivity
simulation
acceptance criteria
Decision
Challenges

## Slide 11: Elements of any PFM Analysis The Analysis Itself
Inputs
acknowledging
the probability of
failure
Models
connectivity
simulation
acceptance criteria
Decision
Challenges
Notes: MM comment on “acceptance criteria” In OFM this is use as a level corresponding to an estimated level of remaining life that is implied as safe enough.

## Slide 12: Elements of any PFM Analysis The Analysis Itself
Inputs
 communication
 policy
Models
connectivity
simulation
acceptance criteria
Decision
Challenges

## Slide 13: Elements of any PFM Analysis The Process
Specifying how the PFM model will be used
Definition & documentation of the component parts of the overall model
Uncertainty characterization and quantification
Software development, documentation, & tracking
PFM model understanding and refinement
Review & approval of PFM model
Regulatory Decisionmaking
With deterministic methods, the process (e.g., consensus codification) helps build
confidence in, &
the efficiency of
current practices.
Goal for PFM: Build confidence, efficiency, and acceptance through process improvement.
Notes: Specifying how the PFM model will be used
  Define metric used to track aging
  Define a ‘failure’ probability screening criterion relatable to this metric
Definition, documentation, and representation of the component parts of the overall model
  Inputs
  Individual models within the PFM
  Model and input connectivity
Definition of uncertainty characterization and quantification
  Which variables and models are represented stochastically, and why? Proper characterization of uncertainty types (aleatory and epistemic).
  Which variables and models are represented as single and/or conservative values, and why?
  Check uncertainty propagation through the PFM model to eliminate double counting.
  Check model validation and model error assessments
  MM: In data, models (form and parameters), and endurance limits. This includes uncertainties in qualification too (e.g., FEM computational errors)
Software development, documentation, and tracking
  Software requirements document
  Software quality assurance and version tracking
  Software verification and validation (V&V)
PFM model understanding and refinement
  Sensitivity studies
  Engineering evaluation of trends predicted by the PFM code
Review and approval of PFM model
  By subject matter experts
  By regulatory staff
  By external stakeholders
Regulatory Decisionmaking
  Consider factors other than the PFM result (e.g., defense in depth, redundancy, periodic inspections, repair of aging and damaged locations).

## Slide 14: On-Going Literature Review Goals and Process
Comprehensive search using modern library tools (Zotero)
  Captures work done by researchers who could not attend this meeting 
Investigating PFM applications from nuclear and other industries involving
  Large expensive structures
  High consequences after structural failure
Identify
  Key common features, best practices, & successful applications
  Areas needing improvement
Special attention paid to previous work done on
  Broad-based and integrated applications
  Efforts to codify / systematize PFM evaluations

## Slide 15: Summary & Next Steps
Use of PFM as a tool for safety assessment of nuclear structures expected to increase in the future
  Demonstrate safety margins for long-term operation
  Quantification of conservatisms of existing methods
This literature survey begins a 2-year duration project for CNSC
Project aim is to identify guidelines for best PFM practices

## Slide 16: Acknowledgement
This work was funded by the Canadian Nuclear Safety Commission under R&S project R690.1
(Contract #3000692560)
The views expressed herein are those of the authors and do not represent official positions of the Canadian Nuclear Safety Commission