## Slide 1: Development of NRC Guidance on Probabilistic Fracture Mechanics for US Nuclear Applications
Patrick Raynaud
Senior Materials Engineer
U.S. NRC Office of Research

## Slide 2: Probabilistic Fracture Mechanics (PFM) at the NRC: A Little Bit of History…
Historical reliance on deterministic fracture mechanics and conservatisms
Risk-Informed policies in place since the mid-1990s
Gradual shift to probabilistic approaches and best-estimate with quantified uncertainties
Recent increased use of probabilistic methods
  Unanticipated factors
  Risk informed cost benefit analyses
  Plant aging, license extensions: highly conservative safety factors impractical for plant life extension

## Slide 3: NRC’s Current Research on PFM: Motivations
Increased complexity of probabilistic analyses and associated regulatory difficulties
  Importance of QA and V&V
  Cultural change in engineering approach
NRC’s PFM tools for component integrity assessment
  FAVOR (1994-Present)
  xLPR (2009-Present)

## Slide 4: PFM Best-Practices Guidance Development
NRC research project to develop best-practices guidance for PFM code development and analyses
Objectives:
  Develop a robust technical basis for PFM codes and analyses
  Provide guidance on desirable attributes for PFM tools in view of regulatory acceptance
  Provide guidance on acceptable methodologies for PFM analyses in support of licensing actions
  Remediate difficulties in reviewing industry submittals using PFM
Technical Letter Report on NRC’s preliminary thoughts on increasing confidence in PFM analyses publicly available at ML18178A431
Focus of this presentation is on developing a graded approach for PFM submittals

## Slide 5: Graded Approach Overview
Based on EPRI’s white paper on minimum contents for PFM submittal
  Supplemented with additional contents and explanation from NRC
  EPRI BWRVIP 2019-016 white paper: “Suggested Content for PFM Submittals to the NRC”, ML19241A545
    All content in green boxes in subsequent slides is from EPRI BWRVIP 2019-016 white paper
Performed cross-walk between NRC’s steps for PFM analysis and EPRI white paper
Analyzed proposed thresholds/considerations for when additional information would be required
Created bins for software QA and V&V

## Slide 6: PFM Submittal Recommended Minimum Contents (NOT Requirements) [1/3]
Software information made available to NRC staff with PFM submittals
  Need to be able to access the code in following cases
    High safety significance
    Generic application of plant specific code
    Complex code
    Extent of differences with codes previously approved by NRC
  In person or virtual audits
Models
  May need more details in these cases:
    New failure mode
    Emergent vs. ongoing: extent of plant experience and Operational Experience for new phenomena
    Implications of unknowns

## Slide 7: PFM Submittal Recommended Minimum Contents (NOT Requirements) [2/3]
Inputs
  Provide basis for categorization of uncertainty between epistemic and aleatory
Convergence
  Make sure convergence is achieved for Quantities of Interest (QoI), not necessarily for other things we don’t care about
  Justify why sampling uncertainty is small enough for intended purpose
Input Importance and Sensitivity Studies
  Document following details
    Sensitivity Analysis (SA) technique, assumptions, and results
    Which QoI are the rankings based on?
    Explain how SA results influenced subsequent analysis
  Describe sensitivity studies

## Slide 8: PFM Submittal Recommended Minimum Contents (NOT Requirements) [3/3]
Verification and Validation
  Allow for audit of software QA documentation
  Identify different code categories (see next slide)
Uncertainty propagation and output uncertainty characterization
  Describe output uncertainty characterization for QoI
Acceptance Criteria
  PFM outputs should be relevant for desired regulatory outcome
  Acceptance criteria are beyond scope of NRC’s PFM guidance but should be derived based on risk informed decisionmaking principles
    RG-1.200
    RG-1.174

## Slide 9: Software QA and V&V Categories
Category 1: NRC approved code
  Category 1A: NRC approved or endorsed code within validated range
    Demonstrate code applicability within validated range
  Category 1B: NRC approved or endorsed code outside of validated range
    Provide justification for new applicability range (additional V&V?)
  Category 1C: Modified NRC approved or endorsed code
    SQA summary and V&V description for modified portions of the code
    Demonstration that the code was not ‘broken’ as a result of changes
    Detailed documentation available for further review upon request (audit)
Category 2: commercial off-the-shelf (COTS) software designed for the specific purpose of the application
  Generally not Excel, GoldSim, FE software
    Demonstrate code applicability
    Description of the software and its pedigree
    Software and documentation available for review upon request (audit)
Category 3: custom code
  Summary of SQA program and implementation (standards?)
  Summary of V&V activities (data, benchmarking…)
  Very simple applications: provide source code instead of standardized SQA and V&V?
Normal care needs to be taken for pre and post processing codes…

## Slide 10: Considerations for Submittal of Additional Depth of Information [1/3]
NRC would encourage pre-submittal meeting to provide direction on which areas might require additional work in the submittal
Safety significance
  In general, level of detail should scale with the safety significance while still taking into consideration the recommended minimum contents
  The recommended minima are satisfactory for class 1 components, and thus also sufficient for lower class components
  The extent to which some recommendations may be relaxed should inversely scale with the complexity and novelty of the application
Failure mode
  Highly energetic failure mode, impact on other systems or on the safety of personnel, poorly understood failure mode, newly modeled phenomenon
  Impact on submittal
    Higher emphasis on model description
    Better description of model inputs
    Better documentation of sensitivities of model
Code complexity
  High number of I/O, large number of phenomena modeled, many code model interdependencies, complex interactions between different physics in the code
  Impact on submittal
    More sensitivity studies to ensure behavior is well understood
    More robust SQA and V&V
Depth of additional information
Safety significance
Failure consequences
Code complexity

## Slide 11: Considerations for Submittal of Additional Depth of Information [2/3]
Margin to acceptance criteria
  Does 95th percentile cross threshold?
  Impact on submittal:
    Higher emphasis on input distributions for low margin
    Better documentation of output uncertainty (tails) for low margin
    Potential relaxation of convergence requirements if lots of margin
Plant specific vs. generic
  Additional information for generic applications
  Baseline level of information for plant specific applications
    Exception: if plant has unique feature requiring special software or inputs
  Impact on submittal:
    Additional proof that inputs cover wide range of generic application
    Additional proof that models cover wide range of generic application
    For plant with unique feature, additional description of specialized software and inputs
Implications of potential unknowns
  If perceived uncharacterized uncertainties are high, recommend additional sensitivity studies
  The higher the consequence, the broader the scope of investigation
Difference from ASME requirements
  The bigger the difference, the more additional information may be needed
Depth of additional information
Margin
Number of plants impacted
Implication of unknowns
Difference from ASME
NRC would encourage pre-submittal meeting to provide direction on which areas might require additional work in the submittal

## Slide 12: Considerations for Submittal of Additional Depth of Information [3/3]
Emergent or ongoing issue
  Emergent issues require more information than ongoing issues
  Impact on submittal:
    Better documentation of inputs and models
First of a kind vs routine applications
  First of a kind applications require more information than routine applications
  Impact on submittal:
    Better documentation of inputs and models
    Better characterization of importance and sensitivities
Change to plant licensing basis
  More information required if plant licensing basis is impacted
  Impact on submittal:
    Better documentation and characterization of margins via uncertainty analysis as well as sensitivity analyses and studies
    PRA requirements
PFM sole basis vs. supporting basis of submittal
  If other supporting analyses, relax recommendations
  Impact on submittal
    Less need for sensitivity analyses and sensitivity studies if other analyses to show trends, etc.
Depth of additional information
Emergent Issue
First-of-a-kind
License Amendment
Ongoing Issue
Routine
Relief Request
Sole basis
Supporting basis
NRC would encourage pre-submittal meeting to provide direction on which areas might require additional work in the submittal

## Slide 13: Summary of NRC’s Proposed Graded Approach for PFM Regulatory Submittals in the US
NRC used EPRI’s proposed contents for a PFM submittal as a starting point
  EPRI BWRVIP 2019-016 white paper: “Suggested Content for PFM Submittals to the NRC”, ML19241A545
NRC adopted the majority of EPRI’s recommendations and added recommendations where deemed necessary and appropriate
NRC defined a categorization scheme for PFM software, and described recommended supporting information for each category
NRC reviewed EPRI’s recommended considerations for submittal of additional depth of information and provided additional guidance where deemed necessary and appropriate

## Slide 14: Next Steps in NRC’s Development of PFM Guidance for US Regulatory Applications
NRC is in the process of developing final drafts of a Regulatory Guide and supporting NUREG technical bases
  Contents will follow the general principles described in Technical Letter Report on NRC’s preliminary thoughts on increasing confidence in PFM analyses (publicly available at ML18178A431)
  A graded approach for PFM will be recommended (starting point is EPRI recommendations from “Suggested Content for PFM Submittals to the NRC”, publicly available at ML19241A545)
Once documents are finalized and internal concurrence is obtained, NRC will hold public meeting to describe the draft guidance
Process for publication of the PFM Regulatory Guide will include chances for stakeholder feedback

## Slide 15: Acknowledgements
NRC wishes to acknowledge EPRI’s important contributions to the PFM guidance project, through public interactions and feedback, and especially through the development of their white paper on “Suggested Content for PFM Submittals to the NRC”
NRC staff involved in the PFM Guidance project: David Rudland, Stephen Cumblidge, Mike Benson, Matt Homiack, Mark Kirk (now at PEAI and CRIEPI)
Sandia National Labs staff involved in the project: Mike Starr, Nevin Martin, Remi Dingreville, Nevin Martin (SNL), Lauren B. Hund, Zach Stuart, John R. Lewis, Josh Mullins, Dusty Brooks, Aubrey C. Eckert-Gallup
Emc2 staff involved in the project: Cedric Sallaberry, Bob Kurth, Elizabeth Kurth