## Slide 1
Probabilistic Working Principles – A UK Nuclear Structural Integrity Perspective
ISPMNA 2019
Mike Martin, Engineering Associate Fellow – Structural Integrity
22nd October 2019

## Slide 2: Introduction and Context
01
Target Reliability Approach
02
Working Principles and Methods
Summary and Next Steps
03
Case Studies
04
05

## Slide 3
Introduction and Context
01

## Slide 4
Hosted by UK FESI and freely available to download from www.fesi.org.uk
Document developed by UK Nuclear Sector Working Group formed from leading industry and academic specialists
Presented at IMechE / FESI event in UK (2018) and webinar (2019)

## Slide 6: Existing Codes, Standards and Regulatory Guidance
IAEA Safety Fundamentals
IAEA Specific Safety Guides
UK ONR Safety Assessment Principles
UK ONR Technical Assessment Guides
TAGSI (Technical Advisory Group on Structural Integrity) advice
National and international codes and standards

## Slide 7
….an adequate margin….
….suitably conservative…
….demonstrably conservative….
….very unlikely….
commentary from existing guidance

## Slide 8
….an adequate margin….
….suitably conservative…
….demonstrably conservative….
….very unlikely….
probabilistic approach is less safe than deterministic
deterministic is all inputs set to worst-case bounding values
why change what’s worked?
some common misconceptions!
commentary from existing guidance

## Slide 9
Target Reliability (Probabilistic) Approach
02

## Slide 10: Application to Service and Design
Service management
Deterministic approach fails
Observed failures
Product design
System understanding
Efficient use of data

## Slide 11: Quantification of Margin

## Slide 12: System Trade of Margin
Expensive difficult tests
Improved mechanistic life prediction
Geometry and manufacturability
Inspection technique and data
In-service data
Target reliability

## Slide 13: Service Management

## Slide 14
Working Principles and Methods
03

## Slide 15: Nuclear SI Probabilistics Working Group
Complements ongoing Nuclear industry initiatives to challenge the perception of probabilistic approaches in structural integrity
Develop an industry guidance document
  Define terminology, common language
  Probabilistic working principles
  Provide context and case studies, describe benefits and limitations
Provides basis for further discussion

## Slide 16: Group Collaboration from UK Nuclear Sector
Working Group
Rolls-Royce
EDF
UKAEA
NNL
Wood
TWI
University of Bristol
Imperial College London

## Slide 17
What it is….
A source of worked examples
What it isn’t….
A code or standard
Endorsed by the nuclear regulatory community
Endorsed by IMechE
The collective view of UK industry and academic experts
A source of guidance and principles for all plant types
Endorsed by contributors’ parent organisations
A link to key references
Foundation for further discussion

## Slide 18
What it is….
A source of worked examples
What it isn’t….
A code or standard
Endorsed by the nuclear regulatory community
Endorsed by IMechE
The collective view of UK industry and academic experts
A source of guidance and principles for all plant types
Endorsed by contributors’ parent organisations
A link to key references
Foundation for further discussion

## Slide 19: Working Principles Document Content
Motivation and Background
Objectives and Scope
Probabilistic Working Principles
Compendium of Examples
Codes, Standards and Regulatory Guidance
Terminology and Techniques

## Slide 20: Probabilistic Working Principles
Why, When and Where?
Margins quantified on reliability basis
Efficient use of data (test, manufacture, inspection)
How to Apply?
Hierarchy of techniques
Validation and Future Requirements
Trade of margin unlocked
Distributions
Mechanistic understanding of failure modes
Verification and Validation
Codes and standards development
Target reliability

## Slide 21: Probabilistic Working Principles
Why, When and Where?
Margins quantified on reliability basis
Efficient use of data (test, manufacture, inspection)
How to Apply?
Hierarchy of techniques
Validation and Future Requirements
Trade of margin unlocked
Distributions
Mechanistic understanding of failure modes
Verification and Validation
Codes and standards development
Target reliability

## Slide 22: Hierarchy of Assessment Techniques
3
Level 3
Pf calculated explicitly, eg Monte Carlo
2
Level 2
Pf calculated approximately, eg FORM
1
Level 1
Pf not calculated directly, eg PSF
R Bullough, VR Green, B Tomkins, R Wilson, JB Wintle, A review of methods and applications of reliability analysis for structrual integrity assessment of UK nuclear plant, Int. J. Pres. Ves. Piping 76 (1999) 909-919

## Slide 23: Probabilistic Fracture Mechanics (R6) Monte Carlo Level 3 Approach

## Slide 24: Partial Safety Factors (PSFs) Level 1 Approach

## Slide 25: First Order Reliability Method (FORM) Level 2 Approach

## Slide 26: Typical Monte Carlo / Finite Element Response Surface Approach

## Slide 27: Target Reliability Derivation
Topic for further work
Reverse PSA for component, region and failure mode specific target
Develop accepted values based on safety classification
Introduce time dependency to PSA
Initiating Event Frequencies
Human Factors
Probabilistic Safety Analysis
(PSA)
See ONR SAPs
Core Damage Frequencies

## Slide 28: Target Reliability Derivation
Topic for further work
Reverse PSA for component, region and failure mode specific target
Develop accepted values based on safety classification
Introduce time dependency to PSA
Initiating Event Frequencies
Human Factors
Probabilistic Safety Analysis
(PSA)
See ONR SAPs
Core Damage Frequencies
reverse approach

## Slide 29: Distributions and Sampling
Aim for distributions (pdf) to be as accurate as possible, minimise ‘input conservatism’, and applicable to data type - histograms as alternative
Margin based on ‘output conservatism’ and required target reliability
Form of distribution important, particularly if trials of interest outside of data - sensitivity studies helpful
Influence of tails can be reduced by using more variables
Latin Hypercube sampling efficient and widely used, numerous approaches available, active research field
Standard approaches for correlation and random numbers

## Slide 30: Verification and Validation
Well-established techniques (eg Monte Carlo, Latin Hypercube) with numerous in-house / commercial applications
Verification important, eg independent code (time consuming)
Validation of physical models consistent with traditional approach
Validation precedent from other high-integrity industry with observed structural-integrity failures (eg: aerospace, rail)

## Slide 31: Terminology and common language….
deterministic
margin
conservative
best estimate
BEPU
nominal
uncertainty
UQ
target reliability
confidence level
PFM
response surface
Monte Carlo
aleatory
epistemic

## Slide 32
Anticipated use
Reference for terminology, techniques and existing information sources
Shows how to quantify margin on a reliability basis
Application in parallel with traditional approaches to build experience, awareness and capability
Basis for further discussion and codes / standards development

## Slide 33
Case Studies
04

## Slide 34: Case Studies
Case studies provided by Rolls-Royce and NNL, using Monte Carlo approach:
  PWR related
  Highly Active Effluent Tank evaporator heating coils
AGR superheater tubing bifurcation inspection using Monte Carlo approach
Other case studies under development, opportunity for others to get involved. Possibly separate document.

## Slide 35: PWR Welded Structural Component
Change in manufacturing process resulted in change to a key material property distribution
Deterministic assessment based on 99.9% bound to data
7% change to 99.9% bound, increased deterministic stress by 2%
Monte Carlo analysis demonstrates mean stress increased by 40% increasing failure probability by order of magnitude
Provided evidence to focus on manufacturing

## Slide 36: PWR Welded Structural Component
change in material distribution
change in stress distribution

## Slide 37
Summary and Next Steps
05

## Slide 38: Summary
Document shows how well-established methods can be used to quantify structural reliability
Opportunity to focus resources
Provides basis for increasing awareness and understanding
Opportunity for codes and standards development for current and future plant types
Document hosted by FESI at www.fesi.org.uk

## Slide 39: Next Steps Focus
Target Reliability Derivation + ASME Link
Codes and Standards Development
Component and System-Level Aggregation
Data Challenge
Perception – particularly Safety Perspective
Responsibilities and Education
More Case Studies
Physics-Based Failure Models and Validation

## Slide 40
Thank you for your attention!
michael.martin@rolls-royce.com