## Slide 1
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Olivia Tuck

## Slide 2
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Introduction
Integrated five-year Nuclear Innovation Programme for the UK
Department for Business, Energy & Industry Strategy (BEIS)
  Advanced Manufacture and Materials
  https://www.gov.uk/guidance/funding-for-nuclear-innovation
EDF Energy
  R5 and R6 guidance documents (UK)
Rolls-Royce
  Nuclear Structural Integrity Probabilistics Working Group
  https://www.fesi.org.uk/news/nuclear-structural-integrity-probabilistics-working-principles/
Literature review to assess the application of probabilistic methods for Volume 2&3 of the R5 procedure

## Slide 3
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
R5 Procedure
R5:
“advice for the assessment of the structural integrity of components that operate at temperatures sufficiently high for creep to occur”
Volumes 2&3 – creep-fatigue crack initiation in defect-free structures
Probabilistics appendix
(EDF Energy Nuclear Generation Ltd., Assessment Procedure R5, Volume 2/3, 2014, Issue 3), (EDF Energy Nuclear Generation Ltd., Assessment Procedure R5, Volume 2/3, Appendix A15, 2018, Draft 2)

## Slide 4
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Probabilistic assessment
Accounting for uncertainty
Benefits
  Incorporate uncertainties
  Avoid bounding cases
Disadvantages
  Computationally expensive
  Regulators / customers
Inputs
Probability of failure

## Slide 5
5. Assessment based on random inputs
6. Repeat 4 and 5
7. Calculate failure probability
8. Convergence
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
R5 Volume 2 & 3 probabilistic appendix
1. Specify information required
2. Distribution choices
3. Failure condition
4. Random sample of inputs
10. Impact of correlations
11. Report results
9. Sensitivity analysis

## Slide 6
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 2 - Parameter and distribution choices
Uncertainties:
Geometry
Load history and service cycles
Material properties
(Kim and Shim, 1998), (Schmitz 2017), (Roy et al., 2010) (Holt and Bradford, 2012), (Zentuti et al., 2018), (Bradford, 2014)
Distributions:
Continuous distributions
Distributions with set maximum and/or minimum
Raw data
Other things to think about:
Time dependencies
Correlation between parameters

## Slide 7
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 4 - Sampling
Monte Carlo
  Simple random sampling
Latin hypercube
x |  |  | 
 | x |  | 
 |  | x | 
 |  |  | x
x |  |  | 
 |  | x | 
 |  |  | x
 | x |  | 
x |  |  | 
 | x |  | 
 |  |  | x
 |  | x | 
Orthogonal sampling
(BOMEL Limited for the Health and Safety Executive, 2001), (Olsson et al., 2003)

## Slide 8
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 4 – Sampling (2)
“Number of simulations should be at least an order of magnitude greater than 1/Pf”
Pf = probability of failure
Pf of 0.01 requires at least 1000 simulations
(Cannell et al., 2016)

## Slide 9
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 8 - Convergence
Confirm convergence:
Monitor convergence as simulation proceeds
Run multiple times and check results
Run with different numbers of simulations
Figure from RAW Bradford and PJ Holt, Int J Pressure Vessels and Piping, 2013.
(Schmitz, 2017), (Bradford and Holt, 2013)

## Slide 10
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 9 – Sensitivity analyses
Sensitivity analyses:
Correlations between inputs and outputs
Quantifying effects of changing inputs
Correlations
(BOMEL Limited for the Health and Safety Executive, 2001), (Bradford and Holt, 2013), (Zentuti et al., 2017), (Bradford, 2014), (Jhung et al., 2005), (Katsuyama et al., 2014)
Other sensitivities:
Tails
Code/implementation

## Slide 11
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Step 11 – Reporting results
R5 Vol 2/3 probabilistics appendix:
Parameter distribution information
Assumed correlations
Coding used to implement Monte Carlo
Outcome of convergence tests
Response surface methods
Reduction of variables
Histograms of parameters of interest
Probability of failure
Results on sensitivity studies
Interpretation
(Vojdani et al., 2018)

## Slide 12
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Other
Software, implementation and verification
(Bradford, 2014), (Jhung et al., 2005), (Katsuyama et al., 2014), (Nuclear Structural Integrity Probabilistics Working Group, 2019), (Sousa et al., 2019), (Ibisoglu and Modarrres, 2015), (Zentuti et al., 2017)
Figure from Nuclear Structural Integrity Working Principles, April 2019, https://www.fesi.org.uk/news/nuclear-structural-integrity-probabilistics-working-principles/
Bayesian techniques

## Slide 13
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Other (2)
Other probabilistic/Monte Carlo methods
(Duan et al., 2015), (Bullough et al. 1999)
Nuclear vs non-nuclear
Figure from X. Duan et al., Nuclear Engineering and Design 2015

## Slide 14
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Summary
Distributions
Fixed values
Correlations
Sampling techniques
Number of simulations
Convergence
Verification
Probabilistic appendix: Other:
Coding
Sensitivities
Probability
of failure

## Slide 15
Review of probabilistic methods relating to Volume 2 & 3 of the R5 procedure
Thank you, any questions?