## Slide 1
Target Reliability Informed Design Optimisation
ISPMNA 2019
Peter Reed, Core Stress Engineer
Rob Marshall, Principal Engineer Core Structural Integrity
22 October 2019
The information in this document is proprietary and confidential to Rolls‑Royce and is available to authorised recipients only – copying and onward distribution is prohibited other than for the purpose for which it was made available

## Slide 2: Introduction and Background
01
02
Target Reliability Approach
03
Higher Level Safety Case
04
Next Steps, Conclusions, Questions?

## Slide 3
Introduction & Background
01

## Slide 4
Introduction & Background

## Slide 5
Introduction & Background
Design
Manufacture
Service Life
Decommissioning
Probabilistic Safety Justifications made for in-service product
Probabilistic Safety Justifications made at design stage for optimised design
Influencing design and optimising through the use target reliability methods
What is the impact of optimisation on the whole system safety case?

## Slide 6: Problem
Introduction & Background
Welded Component (eg. pipe section)
Sharp features in weld underbead.
Justifiable?

## Slide 7: “Deterministic” Assessment
Introduction & Background
Geometric parameters
Material parameters
Performance
parameters
Stress Intensity Factor

## Slide 8: “Deterministic” Assessment
Introduction & Background
Traditional Approach
Set each parameter to its perceived worst case.
Upper or lower bound, based on tolerances or statistical analysis of as-built data
Reserve factor less than 1.00. Crack like geometry not tolerable within the design.

## Slide 9: Problem
Introduction & Background
Machining operation causes damage to other components
Machine out weld geometry
Machining operation can expose buried defects from the welding process.

## Slide 10
Introduction & Background
Cost
Quality
Delivery
ALARP/ALARA Safety Case
Desired Performance
Machining is costly
Machining is time consuming
Machining generates inspection

## Slide 11: Suitably “Deterministic”?
Introduction & Background
KLIM
K
?
Stress Intensity (MPa √m)

## Slide 12
Target Reliability Approach
02

## Slide 13
Target Reliability Approach
Probabilistic Framework (FORM)
Design of Experiments – 256 FE Runs
System Representation (Surrogate Model)
?
1
2

## Slide 14: Probabilistic Inputs in the Design Stage, options?
Target Reliability Approach
Use Capability Analysis (Process capability index, Cpk).
Use historic data from previous manufacturing campaigns.
Perform variation studies to guard against “cliff edge” effects.

## Slide 15: Assumed Level of Capability
Target Reliability Approach
LSL
USL
µ
USL- µ
Assuming a nominally centred, normally distributed process
Cpk targets of 1.33 and beyond.

## Slide 16: Assumed Level of Capability
Target Reliability Approach

## Slide 17: Process Drift Studies
Target Reliability Approach

## Slide 18: First Order Reliability Method
Target Reliability Approach
Monte Carlo
Allows complex systems and non-normal distributions
FORM
Rapid, but requires several assumptions
Near instantaneous run time. Ideal for sensitivity studies. Validated against Monte-Carlo with near perfect agreement.
Used for
this
assessment

## Slide 19
Target Reliability Approach
Previous “Deterministic” Case (RF = 0.85)
Probability beyond 1e-20
Un-machined design, RF all > 1.00 at Cpk > 0.8
K

## Slide 20
Target Reliability Approach

## Slide 21: Summary
Target Reliability Approach
Sensitivity Studies to parameter variation demonstrate tolerance to leaving geometry un-machined.
Machining is being conducted to guard against a failure predicted to be of the order of 1e-13
What is the target reliability?
What is an appropriate level of risk?

## Slide 22
Higher Level Safety Case
03

## Slide 23
Higher Level Safety Case
Interdependencies between failure modes with variation of the same parameters.
Overall probability of system failure is of concern. How do we aggregate failures?

## Slide 24: Systems Approach
Higher Level Safety Case
Review FMEA, identify failure modes and effects.
Understand interdependencies.
Understand links between fracture events and failure.
Understand consequences.

## Slide 25
Higher Level Safety Case
Component 1
Structural Failures
Failure Progression
Failure Mode 1
Failure Mode 2
Failure Mode 3
Overall System Failure
Component 2
Failure Mode 4
Failure Mode 1
Failure Mode 3
Failure Mode 2
Component 3
Failure Mode 2
Failure Mode 1
Failure Mode 3
10-1
10 independent failure modes
10-5
Design stage, apportion an equal reliability per failure mode = 10-5
10-4

## Slide 26
Higher Level Safety Case
Component 1
Structural Failures
Failure Progression
Failure Mode 1
Failure Mode 2
Failure Mode 3
Overall System Failure
Component 2
Failure Mode 4
Failure Mode 1
Failure Mode 3
Failure Mode 2
Component 3
Failure Mode 2
Failure Mode 1
Failure Mode 3
10-1
10 independent failure modes
10-5
Design stage, apportion an equal reliability per failure mode = 10-5
10-4
Bounding Failure progression, different for different failure modes

## Slide 27
Higher Level Safety Case
Component 1
Structural Failures
Failure Progression
Failure Mode 1
Failure Mode 2
Failure Mode 3
Overall System Failure
Component 2
Failure Mode 4
Failure Mode 1
Failure Mode 3
Failure Mode 2
Component 3
Failure Mode 2
Failure Mode 1
Failure Mode 3
10-1
10-5
10-4
Which failure modes are affected by this change?
Is the overall risk tolerable?
Is the impact of the design optimisation safe?

## Slide 28
Higher Level Safety Case
Component 1
Structural Failures
Failure Progression
Failure Mode 1
Failure Mode 2
Failure Mode 3
Overall System Failure
Component 2
Failure Mode 4
Failure Mode 1
Failure Mode 3
Failure Mode 2
Component 3
Failure Mode 2
Failure Mode 1
Failure Mode 3
10-1
10-5
10-4
Overall system failure is improved by design change.

## Slide 29
Next Steps, Conclusions, Questions?
04

## Slide 30: Conclusions
Next Steps, Conclusions, Questions?
Reliability assuming a Cpk of 1.33 | RF for an un-machined component | RF for a machined component
<< 1e-20 (original ‘deterministic’ case) | 0.85 | 1.48
1e-5 (proposed reliability from an aggregated safety case) | 1.20 | 2.15
Effect on other higher level system reliability | Beneficial | Detrimental

## Slide 31: Next Steps
Next Steps, Conclusions, Questions?
Continue to engage with regulatory community.
Monitor manufacturing development with statistical process control.
Live FORM updates based on manufacturing run charts.

## Slide 32
Thank you for your attention!
peter.reed3@rolls-royce.com