## Slide 1: Views on Probabilistic Arguments in Structural Integrity Safety Cases
4th International Symposium on Probabilistic Methodologies for Nuclear Applications (ISPMNA), November 2022
Dr. Christophe Berre CEng, Nuclear Safety Inspector, Structural Integrity

## Slide 2: UK regulatory regime
Goal-setting, non-prescriptive regulatory regime
Onus is on the dutyholder to demonstrate that the risks are reduced ‘so far as is reasonably practicable’ (SFAIRP)
  Case law, 1949: Edwards v Coal National Board
ONR Safety Assessment Principles (SAPs)
ONR Technical Assessment Guide
  TAG/005: Guidance on ALARP
  TAG/016: ‘Integrity of Metal Structures, Systems and Components’
Structure of a safety case
  Independent claims (‘legs’)
  Claims supported by robust arguments and evidence
  Holistic safety case: manufacture, materials, inspections, design assessment, consequences of failure, forewarning of failure

## Slide 3: Graphite core safety case (AGR)
No graphite design code available
  Substantial R&D carried out over many years
  Experimental validation of the models
Safety case legs
  Seismic assessment, graphite oxidation, core monitoring, inspections, lack of cliff-edge beyond design
  Redundancy by design, defence in depth
Core monitoring
  Models have been amended to better represent some observations from the plant
  Example: induced brick cracking due to crack opening

## Slide 4: Expectations for a structural integrity safety case
Demonstration that the risk is SFAIRP
Independent safety case legs
Rigour of the demonstration should be proportional to the consequences of failure
Safety margins against the unexpected
Starting point should be compliance with relevant national and international codes and standards
A probabilistic argument for a structural integrity safety case is unlikely to be acceptable without substantial evidence-based support