## Slide 1: (PM_06) Application of Advanced Importance Sampling Methods for Probabilistic Fatigue Crack Growth Evaluation
Changsik Oh (csoh2011@kins.re.kr)
Sangmin Lee (sangmin.lee@kins.re.kr)
Korea Institute of Nuclear Safety
4th International Symposium on Probabilistic Methodologies for Nuclear Applications
November 1-3, 2022 / Leicester, UK

## Slide 2
Introduction
Problem Definition
Results and Comparison
I
II
III
Conclusions
III

## Slide 3: Introduction

## Slide 4: Background
Variance Control
  Controlling variance is important to obtain accurate estimates of the system’s performance
    The more we know the system, the better variance reduction methods work
    The amount of information depends on problems, analysis tools, skills of engineers, etc.
  In the first simulation stage, we always have a hard time gathering information about the system
    There may be several options for the first simulation stage
      A pilot simulation can be helpful to get information for the second-stage simulation
      Analytical methods such as FORM, SORM, etc. can be useful
      The Adaptive variance reduction method can be a good estimator
    Ultimately, iterative simulations will be necessary

## Slide 5: Background
Importance Sampling
  Importance sampling is a fundamental method to dramatically reduce variance of the estimate
    It may be able to reduce variance by the order of millions
    It often requires a small sample size  low computing cost
  Importance sampling is very efficient for very low probability problems
    Probabilistic fracture mechanics (PFM) problems often have the features as followings:
      Very low probability of Quantity of Interest (QoI)
      Propagation of input uncertainty
      High computing cost

## Slide 6: Objectives
The long-term goal is to find and improve importance sampling schemes for developing Probabilistic Fracture Mechanics Code
  Understanding the theory and implementation
  Test & modification
  Optimization
The objective of this study is to improve understanding of importance sampling methods used in other research fields
  Multiple importance sampling
  Adaptive multiple importance sampling
  Population Monte Carlo

## Slide 7: Problem Definition

## Slide 8: Problem Definition
  Object
  A stainless steel pipe with a single crack
  Aging mechanism
  Fatigue crack growth of an unfound flaw
  Main parameters (1/2)
  Pipe geometry
    12 inch schedule 160
  Initial crack shape
    Circumferential elliptical surface crack
  Fatigue crack growth curve
    pc-PRAISE model
Stainless stees
Stainless stees
When

## Slide 9: Problem Definition
  Main parameters (2/2)
  Fatigue Loads
    Operating state (a): only internal pressure
    Operating state (b): internal pressure + thermal load
  Definition of through-wall
    the crack depth reaches 95% of the thickness
  Stress intensity factor solution
    ASME BPVC Section XI Appendix A (2019 Ed.)
    Weight function method
    Discretization of stress profile

## Slide 10: Problem Definition
(Independent) Random Variables
Random Variables | Distribution | mean | Std. dev. | CV*
Pipe inside radius, Ri [mm] | Constant | 162 | - | -
Pipe thickness, t [mm] | Constant | 36 | - | -
Crack depth, a [mm] | Lognormal | 0.5 | 0.1 | 0.2
Crack half-length, c [mm] | Lognormal | 0.5 | 0.3 | 0.6
FCG coefficient, A [mm/cycle/MPa√m] | Lognormal | 1.59E-10 | 7.95E-11 | 0.5
FCG exponent, n | Constant | 4.0 | - | -
Threshold K, Kth [MPa√m] | Constant | 0.0 | - | -
Peak value of stress profile, Sa,max [MPa] | Normal | 300 | 30 | 0.1
Internal pressure, P [MPa] | Normal | 15.5 | 0.5 | 0.032
*: Coefficient of variable, CV = standard deviation / mean

## Slide 11: Problem Definition: Analysis Method
Monte Carlo Simulation
  Sampling Method
    Simple Random sampling (SRS)
    Latin Hypercube sampling (LHS)
  Variance Reduction Method
    Simple importance sampling (SIS)
    Multiple importance sampling (MIS)
    Adaptive importance sampling (AMIS)
    Population Monte Carlo (PMC)
  Miscellaneous
    No. of simulation: 20
    Time increment: 1 month

## Slide 12: Problem Definition: Reference Cases I
Simple Random Sampling (SRS) & Latin Hypercube Sampling (LHS)
  Sample size: 106 (repetition: 20)
  Higher calculation cost as increasing no. of sampling
  Results of LHS looks like those of SRS
    Performance in variance reduction decreases as sample size increases
      SRS: (8.53×10-5, 8.67×10-6) @ 60 year, Coefficient of Variance (CV) = 0.102
      LHS: (8.53×10-5, 7.37×10-6) @ 60 year, Coefficient of Variance (CV) = 0.086
      Sample size of 106 is not sufficient to estimate very low probabilities
SRS
LHS

## Slide 13: Problem Definition: Reference Cases II
Recap of Simple Importance Sampling (SIS)
  The most fundamental method for variance reduction by concentrating samples on a specific region of interest
  Proposal should be proportional to the integrand  Need good knowledge on the target distribution in advance

## Slide 14: Problem Definition: Reference Cases II
Set-up
  Proposal distribution: student t distribution (mode 3)
    Shifting & scaling using normalization, t5(3, μ, σ=σRV)
Cases
  SIS-1: set the mean of proposal to be the same as the mean of RVs
  SIS-2: SIS-1 + increasing sample size
  SIS-3: set the mean of proposal to be around the target distribution
  SIS-4: set the mean of proposal to fit the target distribution
Case | No. of samples | Mean of proposals |  |  |  | 
 | N | a | c | A | Sa,max | P
SIS-1 | 1,000 | 0.5 | 0.5 | 1.59E-10 | 300 | 15.5
SIS-2 | 10,000 | 0.5 | 0.5 | 1.59E-10 | 300 | 15.5
SIS-3 | 1,000 | 0.8 | 1.4 | 3.98E-10 | 390 | 17
SIS-4 | 1,000 | 0.556 | 0.846 | 6.448E-10 | 369 | 15.58

## Slide 15: Problem Definition: Reference Cases II
Results (SRS+SIS)
  Location of the proposal is important
  Variance decreases as the proposal gets close to the target distribution
    SIS-1: set the mean of proposal to be the same as the mean of RVs
    SIS-2: SIS-1 + increasing no. of simulation
    SIS-3: set the mean of proposal to be around the MPP
    SIS-4: set the mean of proposal to fit the MPP
SRS_SIS-1
SRS_SIS-2
SRS_SIS-3
SRS_SIS-4
Very large variance
Large variance
Decreasing variance as increasing samples
Large variance
Comparable to SIS-2
Very small variance
Decreasing variance as moving to MPP
Increasing sample size
Moving to target
(7.61×10-5,7.23×10-5) @60yr
(8.12×10-5,1.54×10-5) @60yr
(5.87×10-5,4.89×10-5) @60yr
(8.09×10-5,6.30×10-6) @60yr

## Slide 16: Problem Definition: Reference Cases II
Results (SRS+SIS)
  Contribution of random variables
    FCG coefficient & fatigue stress have a greater impact on the estimate than the other random variables
    SIS-1: set the mean of proposal to be the same as the mean of RVs
    SIS-4: set the mean of proposal to fit the MPP
    < SIS-1 >
    : probability density distribution of RVs
    : samples in case of failure
    : samples in case of safe
Proposal for SIS-1 should have a thicker tail
    The border between red & blue samples is clear
    < SIS-4 >
    Samples in red & blue are mixed

## Slide 17: Problem Definition: Reference Cases II
Results (LHS + SIS)
  Results of LHS+SIS are comparable to those of SRS+SIS
SS_SIS-1
LHS_SIS-1
SS_SIS-4
LHS_SIS-4
    SIS-1: set the mean of proposal to be the same as the mean of RVs
    SIS-4: set the mean of proposal to fit the MPP
※ MCS/LHS: 8.53x10-5 @60yr
SRS: (7.61×10-5, 7.20×10-6) @60yr
LHS: (7.44×10-5, 8.14×10-6) @60yr
SRS: (8.09×10-5, 6.30×10-6) @60yr
LHS: (8.56×10-5, 8.91×10-6) @60yr

## Slide 18: Results and Comparison

## Slide 19: Results: Multiple Importance Sampling
Recap of Multiple Importance Sampling (MIS)*
  Deterministic-Mixture (DM): a whole mixture distribution of pre-defined proposal distributions (normally one sample from one proposal)
  Balance heuristic: effective method for weighting proposals
< Balance heuristic >
< Deterministic-mixture >
*: E. Veach, 1997, “Robust Monte Carlo Methods for Light Transport Simulation,” Ph.D. thesis, Stanford University

## Slide 20: Results: Multiple Importance Sampling
Set-up
  Proposal distribution
    Student-t distribution (mode=3), t5(3, μi, σi=σRV)
    Mixture of M proposals evenly distributed within the pre-specified space
  Cases
    MIS-1: set the mixture proposal distribution to cover wide range of area
    MIS-2: MIS-1 + reducing no. of proposal by 1/10
    MIS-2: MIS-1 + reducing no. of proposal by 1/100
    MIS-4: set the mixture proposal distribution to cover narrow range of area around the target distribution
Case | No. of proposal | Samples per proposal | Mean of proposals (min./max.) |  |  |  | 
 | M | Ni | a | c | A | Sa,max | P
MIS-1 | 1000 | 1 | 0.5 / 1.5 | 0.5 / 3.5 | 1.59E-10 / 1.75E-9 | 300 / 600 | 15.5 / 20.5
MIS-2 | 100 | 10 | 0.5 / 1.5 | 0.5 / 3.5 | 1.59E-10 / 1.75E-9 | 300 / 600 | 15.5 / 20.5
MIS-3 | 10 | 100 | 0.5 / 1.5 | 0.5 / 3.5 | 1.59E-10 / 1.75E-9 | 300 / 600 | 15.5 / 20.5
MIS-4 | 100 | 10 | 0.5 / 0.6 | 0.8 / 0.9 | 5.00E-10 / 8.00E-10 | 300 / 400 | 15 / 16
※ Total samples = M x Ni = 1,000
DM

## Slide 21: Results: Multiple Importance Sampling
Results (1/2)
  Variance decreases as the proposal gets close to the target distribution
    Samples away from the target distribution could increase variance
    The range of the mixture distribution should be as narrow as possible
    MIS-1: set the mixture proposal to cover wide range of samples
    MIS-2: MIS-1 + reducing no. of proposal by 1/10
    MIS-2: MIS-1 + reducing no. of proposal by 1/100
    MIS-4: set the mixture proposal to cover narrow range around the MPP
MIS-1
MIS-2
MIS-3
MIS-4
1/10 proposals
1/100 proposals
(6.88×10-5,7.09×10-5) @60yr
(5.96×10-5,3.95×10-5) @60yr
(3.85×10-5,4.6×10-5) @60yr
(8.38×10-5,9.27×10-6) @60yr
※ MCS/LHS: 8.53x10-5 @60yr

## Slide 22: Results: Multiple Importance Sampling
Results (2/2)
  How the balance heuristic works:
    Samples from a good proposal distribution should greatly contribute to the calculation of the estimate.
    Samples from a bad proposal distribution should be ignored in the calculation of the estimate.
  Structural defects:
    Samples in (A) region from the bad proposal distribution in red have weights on the estimate as much as those from a good proposal distribution
    Samples in (B) region from the good proposal distribution in blue don’t contribute to the estimate
(A)
(B)

## Slide 23: Results: Multiple Importance Sampling
Summary
  Deterministic-mixture scheme has no advantage in PFM analysis  requiring high computational cost, but just little variance reduction
  Rough knowledge on MPP in advance
    Poor samples could increase variance
    The range of the mixture proposal distribution should be as narrow as possible
  No. of proposal distributions need to be optimized considering accuracy and computing cost
x18

## Slide 24: Results: Adaptive Multiple Importance Sampling
Recap of Adaptive Multiple Importance Sampling (AMIS)*
  The proposal distribution adapted by updating both its mean & standard deviation based on all the past samples & proposal distributions
  It often requires a small sample size because importance weights from all the past samples and proposal distributions continue to be updated
Sampling @ t :
Calculating importance weight:
Updating the past weights:
Estimating new proposal:
=
*: J.M. Cornuet, J.M. Marin, A. Mira and C.P. Robert, 2011, “Adaptive Multiple Importance Sampling,” Scandinavial Journal of Statistics, 39(4), 798-812

## Slide 25: Results: Adaptive Multiple Importance Sampling
Set-up
  Proposal distribution
    Student-t distribution (mode=3), t5(3, μi, σi=σRV)
  Cases
    AMIS-1: set the initial mean of proposal to be the same as the mean of RVs
    AMIS-2: set the initial mean of proposal to be within the target distribution
    AMIS-3: set the initial proposal to be far away from the target distribution
    AMIS-4: AMIS-3 + increasing sample size by 10 (total samples = 10,000)
※ Total samples = T x Ni = 1,000
Case | No. of iteration | Samples per new proposal | Initial mean of proposals |  |  |  | 
 | T | Ni | a | c | A | Sa,max | P
AMIS-1 | 25 | 40 | 0.5 | 0.5 | 1.59E-10 | 300 | 15.5
AMIS-2 | 25 | 40 | 1.32 | 6.86 | 1.51E-09 | 450 | 18
AMIS-3 | 25 | 40 | 0.271 | 0.081 | 3.45E-11 | 210 | 14
AMIS-4 | 100 | 100 | 0.271 | 0.081 | 3.45E-11 | 210 | 14

## Slide 26: Results: Adaptive Multiple Importance Sampling
Results
  Initial location of the proposal distribution is important
  Little knowledge on the target distribution in advance
    AMIS-1: set the initial mean of proposal to be the same as the mean of RVs
    AMIS-2: set the initial mean of proposal to be within the target distribution
    AMIS-3: set the initial mean of proposal to be far away from the mean of RVs
    AMIS-4: AMIS-2 + increasing no. of samples by 10 (total samples = 10,000)
AMIS-1
AMIS-3
AMIS-4
AMIS-2
Location: Mean
Small variance
Location: opposite direction
Very large variance
Very small variance
Decreasing variance as increasing samples
Location: same direction
Small variance
Increasing sample size
(7.68×10-5,8.55×10-6) @60yr
(7.13×10-5,1.16×10-5) @60yr
(1.38×10-5,2.84×10-5)@60yr
1 simulation failed to converge!
Moving to target
※ MCS/LHS: 8.53x10-5 @60yr
(8.42×10-5,2.65×10-6) @60yr

## Slide 27: Results: Adaptive Multiple Importance Sampling
Summary
  Useful to obtain information on the target distribution
    Initial proposal distribution is fitted to the target distribution after a certain amount of iterations
    Unlike other adaptive methods, the variance of the proposal is also updated
  Little knowledge on the target distribution in advance
    Initial location of the proposal distribution is important
    Poor initial proposal distribution might not be able to converge the estimate
    Sufficient iterations are necessary to converge the parameters of the proposal

## Slide 28: Results: Population Monte Carlo
Recap of Population Monte Carlo (PMC)*
  Samples are generated from importance proposals depending on the previous generated samples
    Importance proposals can be improved by iteration
    Their mean values are updated by resampling from the previous generated samples in respect to their importance weights
*: O. Cappe, A. Guillin, J. M. Marin and C.P. Robert, 2004, “Population Monte Carlo,” Journal of Computational and Graphical Statistics, 13(4), 907-929
Set proposals @ t :
Calculating importance weight & normalizing:
Resampling n values from with replacement:
Updating proposals:
1 sample from 1 proposal @ t :
<Proposals @ t+1>
<Proposals @ t>

## Slide 29: Results: Population Monte Carlo
Set-up
  Proposal distribution
    Student-t distribution (mode=3), t5(3, μi, σi=σRV)
  Cases
    PMC-1: set initial proposals to cover wide range of area
    PMC-2: PMC-1 + increasing sample size by 10 (total samples = 10,000)
    PMC-3: set initial proposals to cover narrow range of area
    PMC-4: PMC-3 + increasing sample size by 10 (total samples = 10,000)
※ Total samples = T x Ni = 1,000
Case | No. of iteration | Samples per proposal | Mean of proposals (min./max.) |  |  |  | 
 | T | Ni | a | c | A | Sa,max | P
PMC-1 | 50 | 20 | 0.5 / 1.5 | 0.5 / 3.5 | 1.59E-10 / 9.54E-10 | 300 / 600 | 15.5 / 20.5
PMC-2 | 50 | 200 | 0.5 / 1.5 | 0.5 / 3.5 | 1.59E-10 / 9.54E-10 | 300 / 600 | 15.5 / 20.5
PMC-3 | 50 | 20 | 0.5 / 0.6 | 0.8 / 0.9 | 5.00E-10 / 8.00E-10 | 300 / 400 | 15 / 16
PMC-4 | 50 | 200 | 0.5 / 0.6 | 0.8 / 0.9 | 5.00E-10 / 8.00E-10 | 300 / 400 | 15 / 16

## Slide 30: Results: Population Monte Carlo
Results
  Initial proposals should be distributed to cover the target distribution
  Need sufficient samples for small variance
    PMC-1: set initial proposals to cover wide range of space
    PMC-2: PMC-1 + increasing no. of samples by 10 (total samples = 10,000)
    PMC-3: set initial proposals to cover narrow range of space around MPP
    PMC-4: PMC-3 + increasing no. of samples by 10 (total samples = 10,000)
PMC-1
PMC-3
PMC-4
PMC-2
Large variance
Large variance
Very small variance
Decreasing variance as increasing samples
Increasing samples (x10)
Increasing samples (x10)
Very small variance
Decreasing variance as increasing samples
(8.99×10-5,2.45×10-5)@60yr
(8.61×10-5,1.30×10-5)@60yr
(8.76×10-5,3.19×10-5)@60yr
(8.07×10-5,9.30×10-6)@60yr
※ MCS/LHS: 8.53x10-5 @60yr

## Slide 31: Results: Population Monte Carlo
Summary
  Useful to obtain information on the target distribution
    Initial proposal distributions are adapted by resampling means from the previous information
    Results are less sensitive to the range of location of the proposal distributions if they can cover the target distribution
  The first simulation is important to obtain meaningful information about the target distribution
    Initial proposals should be distributed to cover the target distribution
    Poor knowledge on the target distribution often requires widely distributed initial distribution  It leads to increase of computational cost (large number of samples and iterations)

## Slide 32: Comparison: Variance
Comparison of Variance
  Convergence speed of AMIS is fastest
    CV @ 60 year: AMIS < MIS < PMC
    Results of MIS is comparable to those of SIS
AMIS
N=10,000
PMC
N=10,000
Method | Mean | Std. Dev. | CV
SIS | 8.48×10-5 | 2.39×10-6 | 0.028
MIS | 8.45×10-5 | 2.44×10-6 | 0.029
AMIS | 8.45×10-5 | 1.58×10-6 | 0.019
PMC | 8.07×10-5 | 9.30×10-6 | 0.115
MIS
N=10,000
SIS
N=10,000

## Slide 33: Comparison: Computing Time
Comparison of Computing Time
  Elapsed time: MIS > PMC > AMIS @ N=10,000
    AMIS and PMC are comparable to SIS  The computational cost of uncertainty propagation is more expensive than those of their complex sampling scheme
  Elapsed time is proportional to the sample size
    As increasing sample size, computing time using MIS increases exponentially
      Computational cost of importance weights for all samples with respect to all proposals is expensive

## Slide 34: Future Work
Generally, PFM problems have a chain of QoIs such as through-wall, leak rates and rupture.
  MIS or PMC could be a good estimator for multi QoIs because the proposals (or samples) are widely distributed  It will require a larger sample size than that for a single QoI
  AMIS looks like a good estimator for a single QoI because its proposal distribution is fitted to a single target distribution
    When other distribution of QoIs are close to the target distribution, their variance would also be reduced
    Iterative simulations for different QoIs with different proposals would be required
Comparison of importance sampling methods for estimating multi QoIs will be performed in the future
  As the system becomes complex, importance sampling methods might be able to show different performances

## Slide 35: Conclusions

## Slide 36: Conclusions
Three different importance sampling methods were investigated via through-wall probability estimation of a pipe subjected to fatigue
  Selecting proposal distributions is the most important to improve the performance of importance sampling methods
    Using multiple proposal distributions is more efficient to infer the information of the system, especially when the prior knowledge is not available
    Adaptive methods reduce the effort in selecting proposal distributions
  Complex sampling schemes are unlikely to be a problem in PFM analysis
    The computational costs of deterministic models seem to be the most expensive

## Slide 37: Conclusions
There is no one-size-fits-all method
  Sampling methods should be chosen considering the complexity of a problem, computational cost, etc.
  Replicating simulations using various methods will be very helpful in understanding the system and obtaining reliable results